Ogden City School District

Request for Proposal

Bonneville Elementary School

Electrical / Telecommunications

RFP

Electrical Power, Surface Raceway,

Equipment Racks, Cable Management,

End to End Category 6, 450 MHz System

1950 Monroe Blvd.

Ogden, Utah

March 17, 2008

Invitation for Proposals

Notice is hereby given that Ogden City School District is inviting proposals to provide services for Bonneville Elementary School (Rooms 6, 8) at 490 Gramercy Ogden, Utah 84401.

Electrical

- Hubbell MT10 Series Raceway

- Hubbell MT10 series accessories where required (boxes, plates, etc.)

- Hubbell Power and Communications Pole (10’ or 15’) as required

- Hubbell S1PT4X4AL, Fire-Rated Poke-Through where required

- Power for 16 computers (4 computers per 20A 120V circuit) per room.

- Two duplex outlets per student station

- Power sub panel if required.  Must support future expansion.

Telecommunications

- Category 6, 450 MHz Plenum cable, all horizontal lines

- Category 6, 450 MHz Patch Cables

- Hubbell patch panels

- Hubbell horizontal wire management

- Hubbell Racks, 2 post with vertical wire management where required

- Hubbell 4 post rack is required for Bonneville (MDF), provide 2 – 2 post Hubbell racks reinforced and set to 32”

- Hubbell category 6 modular jacks (Black)

- Hubbell face plates to match raceway

Bids will be received by the Board of Education of Ogden City School District.  Bids will be in accordance with specifications prepared by Technology Supervisor. Bids will be accepted for combined Electrical and Telecommunications or from separate Electrical or Telecommunications contractors. Combined bid must list Electrical and Telecommunications amounts separately.

The Board of Education of Ogden City School District reserves the right to reject any or all bids or to waive any information or technicality in any bid in the interest of the District.

A Pre-Bid walk through meeting will be held at 2444 Adams Ave. Ogden, Utah 84401 on April 7, 2008.  The meeting will start at 9:00 AM.  We will visit each site after initial meeting and attendance at walk through is mandatory to qualify to bid projects.

Sealed bids must be delivered no later than 2:00 pm Mountain Time April 23, 2008.  Proposals will be accepted in the office of the Purchasing Director at the Ogden City School District Administration Building, Room 209, 1950 Monroe Blvd. Ogden, Utah 84401-0619.

  - Electrical / Telecommunications Proposal

- Scope of work

1.	The contractor (Electrical and or Telecommunications) shall supply all labor and material for a complete functional system as described herein. It will include installing all cabling, conduit or surface molding, faceplates, boxes, 20A 120V circuits, sub panels, power poles, 4x4 Poke-Through, grounding cables, vertical and horizontal wire management, rack mounted patch panels, modular jacks, racks, 2 meter category 6 450 MHz patch cables.

2	Ogden District will provide scaled floor plans and typical classroom layouts.

- The contractor shall test, document and warranty system.

- Equipment

  - Hubbell 2 post rack with vertical wire management

  - Two Hubbell, 2 post racks with supports and vertical wire management to form 4 post rack required for Bonneville in MDF.

  - Hubbell Power and Communications Pole 10’ or 15’ where required, no substitutes.

  - Hubbell S1PT4X4AL, Fire-Rated Poke-Through.  Installs in a 4” diameter core drilled hole where required, no substitutes

  - Hubbell MT10, MediaTrack Surface Raceway. All boxes, faceplates and other accessories must be compatible with MT10 series with no substitutes.

  - Hubbell category 6 patch panels

  - Hubbell category 6 modular jacks (RJ-45)

  - Hubbell horizontal wire management (4 per closet)

  - Labeling is required at technology closets (MDF, IDF) and all termination points.

  - 64, category 6, 450 MHz, 2 meter patch cables

  - Four computers per one, 20A 120V circuit.

  - Two duplex outlets per station (Students table)

  - Power and Communication Pole requires one, 20A 120V circuit with two duplex outlets and four data jacks

  - Where new sub panel is required, up size for future expansion         (ex:  200 Amp panel).

- System Requirements

  - All horizontal cabling will be category 6, 450 MHz plenum cable

  - Maximum horizontal run will be 295 feet

  - 16 data drops per classroom, 4 total rooms

  - Follow the EIA/TIA 568B standard

  - Conduit and or surface molding (no exposed cabling to classrooms except patch cable to device).

  - Grounding cable to all racks

  - All equipment locations specified by Ogden School District Technology Supervisor or Network Engineer only.  No changes without their authorization.

  - Cable support must be provided to specifications in tunnels or ceiling areas.

- Contact Information

  - Contact Ogden School District Technology Supervisor at dont@ogdensd.org