Ogden City School District

Request for Proposal

T.O. Smith Elementary School

Telecommunications / Infrastructure

Request for Proposal

RFP # 2-005

Surface Raceway, Cable Management,

End to End Category 6, 450 MHz System

1950 Monroe Blvd.

Ogden, Utah

January 25, 2012

Invitation for Proposals

Notice is hereby given that Ogden City School District is inviting proposals to provide services for T.O. Smith Elementary School at 3295 Gramercy Ave,

Ogden, Utah 84401.

Telecommunications

- Category 6, 450 MHz Plenum cable, all horizontal lines

- Category 6, 450 MHz Patch Cables

- Hubbell Cat 6 patch panels

- Ladder rack support to wall is required for 2 and 4 post racks

- Hubbell category 6 modular jacks (Voice – Gray, Data - Black)

- Hubbell face plates to match raceway or equivalent

- 24 strand 50 micron fiber

Bids will be received by the Board of Education of Ogden City School District.  Bids will be in accordance with specifications prepared by Technology Supervisor. Bids will be accepted for Telecommunications. Bid must list all Telecommunications line items with quantity and amounts separately.

The Ogden District requires bidding contractors to have Erate SPIN to participate.  This SPIN number must be included on sealed bid document.  This project will follow guidelines and timelines specific to the School and Libraries Division and contingent on all factors.  All work must be completed on or before June 6, 2013.

The Board of Education of Ogden City School District reserves the right to reject any or all bids or to waive any information or technicality in any bid in the interest of the District.  Contractor is liable for damage caused during installation.  The Board of Education of Ogden City School District reserves the right to terminate this project without cause.

A Pre-Bid walk through meeting will start at T.O. Smith Elementary main office at 3295 Gramercy Ave, Ogden, Utah 84401, on February 7, 2012.  The meeting will start at 11:00 AM.  We will visit all rooms after initial meeting and attendance at walk through is mandatory to qualify to bid project.  Documents provided by Ogden District.

Sealed bids must be delivered no later than 2:00 pm Mountain Time February 28, 2012 and contain provided RFP number and SPIN.  Bid must contain itemized listing to verify completeness of proposal. Proposals will be accepted in the office of the Purchasing Director at the Ogden City School District Administration Building, Room 210, 1950 Monroe Blvd. Ogden, Utah 84401-0619.

Bids will be opened Thursday, March 1, 2012 at 2:00 p.m.

  - Telecommunications Proposal

- Scope of work

1.	The contractor (Telecommunications) shall supply all labor and material for a complete functional system as described herein. It will include installing all cabling, conduit or surface molding, faceplates, boxes,  grounding cables, vertical wire management, rack mounted patch panels, modular jacks, racks, 2 meter category 6 450 MHz patch cables, 50 micron 24 strand fiber with LIU and SC termination.

2.	The contractor shall test, document and warranty system.

- Equipment

  - Hubbell horizontal wire management for MDF and IDF (6 each)

  - Add Full height enclosure (on wheels) to new IDF

  - Hubbell category 6 patch panels

  - Hubbell category 6 modular jacks (RJ-45)

  - Labeling is required at technology closets (MDF, IDF(s)) and all termination points. Patch panels and jacks.

  - 2 – 2 meter patch cables, category 6, 450 MHz, per horizontal cable

  - 24 Stand, 50 micron fiber cable, SC termination required MDF to IDF

  - 19” rack mounted SC terminated LIU is required new IDF (MDF)

- System Requirements

  - All horizontal cabling will be category 6, 450 MHz plenum cable

  - Maximum horizontal run will be 295 feet

  - Follow the EIA/TIA 568B standard

  - Conduit and or surface molding (no exposed cabling in classrooms except patch cable to device).

  - Grounding cable to all racks

  - All equipment locations specified by Ogden School District Technology Supervisor or Network Engineer only.  No changes without their authorization.

  - Cable support must be provided to specifications in tunnels

  - Voice over Ethernet Jack must be Gray

  - Data Jack must be Black

  - Top left jack must be Gray at each teacher location

  - All Voice over Ethernet jacks must terminate on their own patch panel

  - Horizontal Cabling: Voice cables must have different color than data.

  - Each data jack location has conduit stubbed to wire type cable tray in hall.

  - Pull out old data line while installing new.

- Provide to all Classrooms

  - 12 new data drops per classroom

  - 6 drops at 2 locations or 4 drops at 3 locations

  - At least two locations in room will required surface molding

    - All molding clips and corners must be included

  - Provide two meter category 6 patch cables (B-6)

- Provide to Computer Lab

  - Replace existing 38 data locations

  - Provide two meter category 6 patch cables (B-6)

- Provide to Media Center

  - Replace 12 existing on left and increase to 20

  - Provide to checkout station, 2-2 drop outlets.

  - Replace all in media office

  - Add power pole and 4 data drops behind interwrite board

  - Add 4 data drops to right side on wall by TV

  - Provide two meter category 6 patch cables (B-6)

- Lunch room

  - Replace existing data location

  - Add one new 4 data drop location

  - Add one new 2 data drop location at ceiling height

  - Provide two meter category 6 patch cables (B-6)

- Provide to all main office locations

  - Replace all existing data locations

  - Wall remodels will add 3-2 data drop locations

  - Provide two meter category 6 patch cables (B-6)

- Add 1 data drop to each room specified on drawing (9 locations)

  - Locate data drop at ceiling height

  - Provide two meter category 6 patch cables (B-6)

- Teacher work room (next to media center)

  - Add 2-4 data drop locations back right corner

  - Add 1-2 data drop locations left of door entry

  - Provide two meter category 6 patch cables (B-6)

- Faculty room

  - Replace existing data drops

  - Provide two meter category 6 patch cables (B-6)

- Portables (8)

  - Rooms 22 – 26 add 3-4 data drop locations

  - Replace fiber to portable IDF with 12 strand, 50 micron

  - Terminate in IDF LIU and at MDF LIU

  - Double wide labs are already Cat 6

    - Replace teacher location with 4 data if Cat 5(e).

- Add new IDF in office room labeled as Nurse

  - Install full height enclosure ( 4-post type) on wheels

  - Add 4 horizontal wire management

  - Add rack SC terminated LIU to support 24 strand, 50 micron, fiber to MDF.  Add LIU to MDF to terminate fiber.

  - Fiber must be in plenum inner duct

  - Add cable support and adequate service loop to support movement of enclosure (3 feet min)

- Contacts / Information

  - Contact Ogden School District Technology Supervisor at dont@ogdensd.org or cell phone 801-430-1283

  - Alternate Contact:  Mike Hipwell hipwellm@ogdensd.org

  - For all documents:  Category 6 cabling, also cat 6