MAINTENANCE DEPARTMENT

OGDEN CITY SCHOOL DISTRICT

2444 ADAMS AVENUE

OGDEN, UT 84401

SPECIFICATIONS	Furnish all labor and materials required for a new parking garage, new space for shipping and receiving, and interior renovations to the existing facility to reconfigure walls at the following location:

New District Maintenance Facility                     956 20th Street

Ogden City School District (OCSD) is expanding and renovating its central maintenance facility, located at 956 20th Street, Ogden, Utah.  The expansion consists of both new building construction and existing building renovation, to include, 1) 140’ x 60’ x 16’h new metal building used for enclosed vehicle parking, to be constructed immediately north of the existing building, 2) 60’ x 50’x 18’h new metal building addition used for shipping and receiving maintenance materials for the school district, and 3) renovations to the existing building to reconfigure office space for new occupants. The existing facility was originally constructed as an industrial education facility (Occupancy Group E) in the 1960s and is currently used for various facilities support function for OCSD, including maintenance shops supporting OCSD real property operations throughout Ogden City.  The new facilities are planned to be architecturally compatible with the existing brick-faced facility, including matching or complementary colors; and, where possible, textures and architectural features, consistent with the practical requirements and economies for a maintenance facility. The present facility is primarily masonry construction, one story, double-width fire-rated walls, and wood deck on steel joist roof system. The completed site will include paved parking lots, sod and shrub landscaping, and numerous mature trees. Facilities maintenance operations do not generate objectionable odors, dust, smoke or noise. Waste streams consist of normal light-duty shop waste materials, which are contracted for disposal through contract service providers using environmentally approved methods. There is a significant open space surrounding the building perimeter which permits allowable area increase for floor space calculations.

Contractor shall have:

- General Contractor’s License

- All Insurances required by the State Law

- Minimum 5 years of steel building erection experience

- Certified Personnel for steel building erection, seams, and sealants

- Personal protective fall gear

- Submit proof of accreditation with a steel building manufacturer or builder

dealer for metal buildings that have membership with Metal Building

Manufacturer’s Association (MBMA)

- An available list of completed steel building projects

- Proof of liability insurance

Additional Information

- Start date for this project will be March 28th, 2013

- Completion date for this project will be July 1st, 2013

- If the project is not complete by July 1st, 2013, there will be a $500 fine

per day for each day the project is not complete

- The Contractor must provide portable restroom facilities

- The Contractor is responsible to clean any dust or debris that has been

created from the construction before project will be considered complete.

- Contractor is responsible to replace or repair any damage to the building or

contents during construction.

- The Ogden School District is a Tobacco/Alcohol/Drug-Free-Zone. There is

a zero tolerance policy in place. No 	smoking, drinking, or drug use is

allowed on any district property.

Contractor must follow all specifications contained in the engineered drawings and any changes or additions as provided by owner.

Purchasing Department                                                                                    RFP #3-004

BOARD OF EDUCATION, OGDEN CITY, UTAH

Room No. 210

1950 Monroe Blvd.

Ogden, Utah

Quote your lowest net price, terms, and time of delivery on the following items F.O.B. Ogden City School District.

Bids will be received until 2:00 p.m. MDT, March 14, 2013.

Furnish and install, as hereafter specified, labor and all materials as hereafter specified, including the furnishing of all labor, plant, equipment, appliances, and material for performing the operation in connection with the construction at the Ogden School District Maintenance Facility

Total Cost for Project				$________________

The price inserted must also include delivery charges, transportation to site and any other surcharge. The price must be good for one year.

BONDS:  A certified check or bid bond of not less than five percent [5%] of the amount of the bid is to accompany the bid. The bid bonds of the unsuccessful bidders will be returned within 5 days after the award of the bid.  The Board of Education will also require a 100% full performance and 100% full payment bonds.

Sealed bids will be received until 2:00 p.m. MDT, March 14, 2013 at the office of the Purchasing Agent Administration Building Room 210, 1950 Monroe Blvd., Ogden Utah 84401. The bids will be open at 2:00p.m. the same day. Envelopes to be marked:  "OGDEN SCHOOL DISTRICT MAINTENANCE FACILITY RFP #3-004."

The Board of Education reserves the right to accept or reject any or all bids or to make an award of contract based on acceptance of other than low bid. The Board of Education also reserves the right to deny bids from contractors that are not in good standing with the Ogden School District.

BIDDER: To complete this information

1. DELIVERY PROMISED _____________________

2. TERMS: Net 30 unless discounts are offered__________________________

3. DATE OF BID _______________________

_____________________________________________

Signature and Title of Person Submitting Bid

____________________________________________

Coordinator of Purchasing Authorized Signature

REQUISITION NO.______________________________

PURCHASE ORDER NO.___________________________

INVITATION TO BID

Sealed bids will be received by the Board of Education of Ogden City School District for the District Maintenance Facility.  Bids will be in accordance with drawings and specifications prepared by Ogden City School District and it may be obtained at the pre-bid walk through. You may also view them at www.ogdensd.org. Click on the “Request for Proposal” button at the bottom of the home page.

A Pre-Bid walk through meeting will be held at the site of the new District Maintenance Facility, 956 20th Street, Ogden, Utah, commencing at 1:00 p.m. on March 6, 2013.  Attendance at this walk-through is mandatory to qualify contractors to bid this work.

The Director of Support Services at the Administration Building Room 210, 1950 Monroe Blvd., Ogden, Utah 84401 will receive bids until the hour of 2:00 P.M. on March 14, 2013. The bid opening will be at 2:00 p.m. the same day. Envelopes must be labeled “OGDEN SCHOOL DISTRICT MAINTENANCE FACILITY RFP         #3-004."

A bid bond in the amount of five percent (5%) of the bid, made payable to the Board of Education of Ogden City School District, shall accompany bid.  If a certified or cashier's check is used in lieu of a bid bond, a certificate from an approved surety company guaranteeing execution of a 100% Performance Bond and 100% Payment Bond must accompany bid. All bidders must be in good standing with the Ogden City School District.

The Board of Education of Ogden City School District reserves the right to reject any or all bids or to waive any informality or technicality in any bid in the interest of the District.

BOARD OF EDUCATION OF OGDEN CITY SCHOOL DISTRICT

KEN CRAWFORD, DIRECTOR OF SUPPORT SERVICES