Ogden City School District

Request for Proposal

Highland Jr. High School

Computer Lab Rm-12

Electrical / Telecommunications

RFP 10-008

Electrical Power, Surface Raceway,

Equipment Racks, Cable Management,

End to End Category 6, 450 MHz System

1950 Monroe Blvd.

Ogden, Utah

December 4, 2009

Invitation for Proposals

Notice is hereby given that Ogden City School District is inviting proposals to provide services for Highland Jr. High School (Room 12) at 325 Gramercy

Ogden, Utah 84401.

Electrical

- Hubbell MT10 Series Raceway where required

- Hubbell MT10 series accessories where required (boxes, plates, etc.)

- Power and Communications Pole (10’ or 15’) as required

- Power for 44 computers (4 computers per 20A 120V circuit) per room.

- 60 AMP circuit with disconnect to support future A/C unit per lab.

- Power sub panel if required.  Must support future expansion.

Telecommunications

- Category 6, 450 MHz Plenum cable, all horizontal lines

- Category 6, 450 MHz Patch Cables

- Hubbell Cat 6 patch panels

- Hubbell Rack, 2 post with vertical wire management

- Ladder rack support to wall is required for 2 and 4 post racks

- Hubbell category 6 modular jacks (Black) (keystone)

- Hubbell face plates to match raceway

- 24 Stand, 62.5 micron multimode fiber cable, SC terminated required

- 19” rack mounted LIU required

Bids will be received by the Board of Education of Ogden City School District.  Bids will be in accordance with specifications prepared by Technology Supervisor. Bids will be accepted for combined Electrical and Telecommunications only. Bid must list Electrical and Telecommunications line items with quantity and amounts separately.

The Board of Education of Ogden City School District reserves the right to reject any or all bids or to waive any information or technicality in any bid in the interest of the District.  Contractor liable for damage caused during installation.

A Pre-Bid walk through meeting will start at Highland Jr. High main office at 325 Gramercy, Ogden, Utah 84401, on January 5, 2010.  The meeting will start at 9:00 AM.  We will visit room after initial meeting and attendance at walk through is mandatory to qualify to bid project.  Documents provided by Ogden District.

Sealed bids must be delivered no later than 2:00 pm Mountain Time January 19, 2010.  Proposals will be accepted in the office of the Purchasing Director at the Ogden City School District Administration Building, Room 209, 1950 Monroe Blvd. Ogden, Utah 84401-0619. Bids must be marked RFP 10-008 on the outside of sealed envelope.  Any bids delivered after 2:00 pm will not be accepted.

  - Electrical / Telecommunications Proposal

- Scope of work

1.	The contractor (Electrical / Telecommunications) shall supply all labor and material for a complete functional system as described herein. It will include installing all cabling, conduit or surface molding, faceplates, boxes, 20A 120V circuits, sub panels, power poles, grounding cables, vertical wire management, rack mounted patch panels, modular jacks, racks, 2 meter category 6 450 MHz patch cables, 62.5 micron 24 strand fiber with LIU and SC termination.

2.	The contractor shall test, document and warranty system.

- Equipment

  - Hubbell 2 post rack with vertical wire management

  - Ladder rack support to wall is required, 2 and 4 post racks

  - Power and Communications Pole 10’ or 15’ where required

  - Hubbell MT10, MediaTrack Surface Raceway. All boxes, faceplates and other accessories must be compatible with MT10 series with no substitutes.

  - Hubbell category 6 patch panels

  - Hubbell category 6 modular jacks (RJ-45) keystone

  - Labeling is required at technology closets (MDF, IDF) and all termination points.

  - 2 – 2 meter patch cables, category 6, 450 MHz, per horizontal cable

  - Four computers per one, 20A 120V circuit.

  - Two duplex outlets per station (Students table)

  - Power and Communication Pole requires 20A 120V circuit (per 4 computers) with two duplex outlets and data jacks as indicated.

  - Where new sub panel is required, up size for future expansion         (ex:  200 Amp panel).

  - 1 – 60 AMP circuit with disconnect per lab for future A/C unit.

- System Requirements

  - All horizontal cabling will be category 6, 450 MHz plenum cable

  - Maximum horizontal run will be 295 feet

  - Follow the EIA/TIA 568B standard

  - Conduit and or surface molding (no exposed cabling to classrooms except patch cable to device).

  - Grounding cable to all racks

  - All equipment locations specified by Ogden School District Technology Supervisor or Network Engineer only.  No changes without their authorization.

  - Cable support must be provided to specifications in tunnels or ceiling areas.

- Room 12

  - Provide and install two post rack in storage room (Room-12)

  - Provide and install 48 port category 6 patch panel

  - Provide and install ladder rack support

  - Provide and install 2 - rack LIU (MDF and IDF)

  - Provide and install 24 strand fiber to MDF and terminate SC

  - Provide 4, 62.5 micron SC to SC patch cables (two meter)

  - Run new category 6 cables to lunch room ( 2 -2 drop locations)

  - Run new category 6 cables to lunch room managers office (2 cables)

  - Run new category 6 cables (2) to wood shop

  - Run 44 data drops to locations provided by drawing, room 12

  - Provide and install 11 power poles

  - Remove all existing drop cables (power) in room 12.

  - Provide and install power for 44 computers at 4 per 20 AMP circuit.

  - Provide and install 1 – 60 AMP circuit with disconnect for future A/C unit.

  - Provide 98, two meter category 6 patch cables

- Contact Information

  - Contact Ogden School District Technology Supervisor at dont@ogdensd.org or cell phone 801-430-1283