OGDEN SCHOOL DISTRICT

REQUEST FOR PROPOSAL

RFP # 9026

The Ogden City School District is requesting proposals from any qualified company for bleachers and player benches to be located at the District Campus and at Highland, Mound Fort, and Mount Ogden Junior High Schools.  The bleachers and benches will be placed on the athletic fields at each of the schools and at the district office in the following manner: One elevated aluminum bleacher with a seating capacity of approximately 75 people at each school; six aluminum player benches each at Highland and Mound Fort and four aluminum player benches each at the District Campus and Mount Ogden; and three aluminum bleachers with a seating capacity of approximately 40 people each at Highland and Mound Fort, and two aluminum bleachers each at the District Campus and Mount Ogden.

The cost of the 3 aluminum elevated bleachers, 20 aluminum player benches with back rests, and 10 aluminum bleachers and all related expenses as included in the specifications listed below can not exceed $72,000.

Elevated bleacher requirements:

Material: Aluminum

Number of Rows: 5

Length of rows: approximately 27 feet

Seating capacity: approximately 75

International building code compliant: Yes

Must include a guardrail system that consists of aluminized chain link fence on the back and sides.

Include shipping: Yes

Include installation: Yes. Including laying a level concrete slab for bleachers to be anchored to, anchoring bleachers, and assembly.

Include ADA ramp on one side and stairs on the other side: Yes

Include a cutout area in bleachers by ramp for ADA access: yes

Minimum Height of front walkway: 2’ 6”+

Portable Player bench with back rest requirements:

Material: Aluminum

Length of bench: approximately 15 feet

Include shipping: Yes

Bleacher requirements:

Material: Aluminum

Number of Rows: 4

Length of rows: approximately 15 feet

Seating capacity: approximately 40

International building code compliant: Yes

Include shipping: Yes

Include installation: Yes

Sealed bids must be delivered to the Ogden City School District Procurement Office, Room 209, Administration Building, 1950 Monroe Boulevard, Ogden Utah 84401 by 11:00AM on Thursday, July 2, 2009.  Please include Bid # 9026 on the outside of your sealed envelope.  Proposals received after 11:00AM will not be considered and will be returned unopened.