Request for Proposal

RFP # 2-007

Telecommunications – Switches / Wireless

Switch support - 10/100/1000

Switch/Modular (Core) Layer 3 Blade Type

Uplink support – 1GB Twisted Pair/Fiber, 10GB Fiber

1950 Monroe Blvd.

Ogden, Utah

January 25, 2012

Table of Contents

Table of Contents…………………………………………………………………………...……………………………… 2

Request for Proposal – Telecommunications / Switches - Wireless…………….…………….……… 3

Introduction………………………………………………………………………………………………………………….. 3

- Overview………………………………………………………………………………….…………………… 3

Proposal Requirements…..................................................................................................................................... 4

- Scope of Work……………………………………………………………………………………….………. 4

- Hardware Specifications………………………………………………………………………………... 4

School Details……………………………………………………………………………………………………………….. 6

- Gramercy Elementary…………………………………………………………………………………… 6

- T.O. Smith Elementary…………………………………………………………………………………... 6

- Mound Fort Jr High……………………………………………………………………………………….. 7

Evaluation Process………………………………………………………………………………………………………... 7

Bid Requirements…………………………………………………………………………………………………………. 8

Proposal Certification…………………………………………………………………………………………………… 8

Request for Proposal

Telecommunications

Switches / Wireless

Introduction

  - Overview

Notice is hereby given that Ogden City School District is inviting proposals to provide services for Telecommunication – Switches and Wireless.

Bids will be received by the Board of Education of Ogden City School District.  Bids will be in accordance with specifications prepared by Technology Supervisor. Bids will be accepted for Telecommunications hardware – Switches, and Wireless controllers and access points.  Bid must contain detailed itemized list.

The Ogden District requires bidding contractors to have Erate SPIN to participate.  This SPIN number must be included on sealed bid document.  This project will follow guidelines and timelines specific to the School and Libraries Division and contingent on all factors.

The Board of Education of Ogden City School District reserves the right to reject any or all bids or to waive any information or technicality in any bid in the interest of the District.  Contractor is liable for damage caused during installation where applicable.  The Board of Education of Ogden City School District reserves the right to terminate this project without cause.

- Scope of Work

The contractor / vendor shall supply new hardware, complete with all manufacture warranties and support.  Refurbished / remanufactured hardware is not eligible for this service proposal.  Provider must be eligible to provide hardware under Utah State purchasing contract pricing.  Vendor must be authorized provider.

- Equipment Specifications

  - Modular (core type) utilizing optional blades with 6 to 9 slots

    - 48 port 10/100/1000 twisted pair supporting in-line power

    - Minimum of 8 port 10GB fiber on a single blade

    - Minimum of 16 port 1GB fiber on a single blade

    - Dual power supply to include 220 VAC support

    - In-line power must support the Cisco 9951 VoIP phone

  - Layer 3 support (MDF – IDF(s))

    - Must support the following routing protocols

      - EIGRP

      - OSPF

  - Layer 2 support (MDF – IDF(s))

    - Multiple VLAN encapsulation

      - Dot1q trunk is required

      - Supports Interface VLAN configuration

  - 48 Port 10/100/1000 with 2 modular uplink ports, and in-line power

    - Uplink modules 1GB twisted pair, 1GB fiber, and 10GB fiber

    - Must be available with in-line power option and without in-line power

    - Must be available to support Layer 3, EIGRP and OSPF

    - Must be available to support Layer 2, multiple VLAN and dot1q trunk

    - Must support Layer 3 or Layer 2 stacking

  - 24 port 10/100/100 with 2 modular uplink ports, and in-line power

    - Uplink modules 1GB twisted pair, 1GB fiber, and 10GB fiber

    - Must be available with in-line power option and without in-line power

    - Must be available to support Layer 3, EIGRP and OSPF

    - Must be available to support Layer 2, multiple VLAN and dot1q trunk

    - Must support Layer 3 or Layer 2 stacking

  - Wireless

    - Wireless LAN controller is required

      - Must have remote web management

      - Must support more than 10 access points

    - Wireless Access Point

      - Must be 802.11/n

      - Must be powered by switch port

- School Details

  - Gramercy Elementary

    - 7 – 24 Port 10/100/1000 + 2 uplink (In-line Power)

    - 11 – 24 Port 10/100/1000 + 2 uplink

    - 10 – 10GB Fiber with support modules

    - 4 – 1GB Fiber with support modules

    - 1 – Wireless LAN controller for up to 12 Access Points

    - 12 – 802.11/n Wireless Access Points

    - 1 – 4 Port FXO module for Cisco 3845 Router

    - All other required items cost/no cost

  - T.O. Smith Elementary

    - 5 – 24 Port 10/100/1000 + 2 uplink (In-line Power)

    - 2 – 48 Port 10/100/1000 + 2 uplink (In-line Power)

    - 1 – 48 Port 10/100/1000 + 2 uplink

    - 12 – 24 Port 10/100/1000 + 2 uplink

    - 6 – 10GB Fiber with support modules

    - 6 – 1GB Fiber with support modules

    - 1 – Wireless LAN controller for up to 12 Access Points

    - 12 – 802.11/n Wireless Access Points

    - 1 – 4 Port FXO module for Cisco 3845 Router

    - All other required items cost/no cost

  - Mound Fort Jr. High

    - 1 – 8 Port 10GB Fiber blade for Cisco 6506

    - 1 – 512MB Compact Flash for 6506

    - 6 – X2 type 10GB modules for 8 Port blade

    - 5 – 24 Port 10/100/1000 + 2 uplink (In-line Power)

    - 18 – 24 Port 10/100/1000 + 2 uplink

    - 4 – 10GB Fiber with support modules

    - 6 – 1GB Fiber with support modules

    - 1 – Wireless LAN controller for up to 25 Access Points

    - 15 – 802.11/n Wireless Access Points

    - 1 – 4 Port FXO module for Cisco 3845 Router

    - All other required items cost/no cost

- Bid Evaluation

  - The following point system will be used to qualify and rank all bids.

    - Up to 20 points will be awarded for year(s) as authorized provider

    - 10 points, Yes/No will be awarded for routing protocol EIGRP

    - Up to 20 points will be awarded based on infrastructure compatibility

    - Up to 20 points will be awarded based on satisfied customer referrals

    - 5 points, Yes/No for Local Support

- Bid Requirements

Sealed bids must be delivered no later than 2:00 pm Mountain Time February 28, 2012 and contain provided RFP number and SPIN.  Proposals will be accepted in the office of the Purchasing Director at the Ogden City School District Administration Building, Room 210, 1950 Monroe Blvd. Ogden, Utah 84401-0619.

Bids will be opened Thursday, March 1, 2012 at 2:00 p.m.

*Contractor / Vendor must submit one (1) original and three (3) copies. Bid must contain itemized subtotal listing per school to verify completeness of proposal within the bid total.

- Proposal Certification

This section must be completed to be considered as valid

_______________________________________________________			________________________

(Authorizing Signature)						(SPIN #)

_______________________________________________________			_______________________

(Typed Name of Authorizing Signature)				(Date)

______________________________________________________

(Title of Authorizing Signature)