Request for Proposal

Demolition- 2100 Madison Ave Site

RFP # 4-007

Ogden City School District

1950 Monroe Blvd.

Ogden, Utah

August 7, 2013

- Intent of Request for Proposals (RFP), Background, and Bid Requirements

  - Intent of Request for Proposals (RFP)

The purpose of this Request for Proposals is to solicit competitive sealed proposals from qualified and experienced individual(s) or firm(s) to provide demolition services for the Ogden School District (OSD). OSD is requesting bids for the demolition and site clearance of all existing structures, together with all associated out buildings and appurtenances (the “Demolition Area”) within a five-acre site located at approximately 2100 Madison Avenue, Ogden, Utah (see Attachment 2, ‘Demolition Area’). The successful Contractor will be expected to provide all tools, transportation, labor, and equipment necessary to perform the required duties herein.  The overall objective of this project is to remove all structures, debris, identified trees, site components, etc. and to leave the ground empty, level, and ready for future development.

1.2	Ogden City School District Background

Ogden School District (OSD) is a highly-impacted school district in the state of Utah.  The District has fourteen (14) elementary schools, three (3) junior high schools, two (2) comprehensive high schools, one (1) alternative high school and one (1) Youth in Custody program.   OSD has approximately 13,000 students and 2182 employees.   The Board of Education consists of seven (7) elected members.  There are three collective bargaining groups – classified, licensed, and administrative. Several of our schools are currently involved in the University of Virginia’s Turnaround Specialist Program that combines their Darden School of Business with the Curry School of Education. After implementing their intense strategies for an academic year, the OSD has seen some successful turnaround results with their faculty and academic success with their students.

1.3 Bid Requirements.

Bids must be sealed and submitted in a timely manner. Bidders shall provide (1) sealed copy of the proposal and it MUST be labeled on the outside with Demolition RFP # 4-007. Proposals must be submitted before 2:00 p.m. on August 27, 2013, to Ogden School District Attn: Purchasing-room 210, 1950 Monroe Blvd. Ogden, UT 84401.  Any proposal received after that deadline will be deemed non-responsive and will not be considered for evaluation. Faxed copies will not be accepted.

Bids must be submitted on this form, and must be typed or written in ink and signed. Bids must be signed by an official of the company authorized to bind the offeror (Please see #9 below). The proposed price shall be good for a period of at least one hundred twenty (120) days from the submittal date. OSD reserves the right to refuse any and all bids and to waive any technicalities and formalities. OSD reserves the right to negotiate with all qualified offerors and reserves the right to cancel this solicitation in part or in its entirety if it is in the best interest of OSD to do so. Any agreement for services is subject to board approval.

A mandatory Pre-Bid walk-through at the demolition site (approximately 2100Madison Ave. Ogden, UT) will occur on August 20, 2013 at 10:00 AM.  Attendance at walk-through is mandatory to qualify to bid project.

Those wishing to submit a bid for the project must provide, at a minimum, the following items:

- Completed bid worksheet (Attachment 1). Note the bid form is laid out in a specific manner. Please structure your bids accordingly.

- Documents showing appropriate certification in eight-hour OSHA Class II asbestos removal.

- Proof of all other appropriate professional licensing as required by the State of Utah

- If applicable, documents showing pre-certification as a woman-owned, minority owned, small, or disadvantaged business

- A disposal and recycling plan for all structures and debris removed from the site

- Proof of Insurance: General Liability, Workers Comp, Automobile (must be current)

This solicitation does not commit OSD to award a contract, or to pay for any cost incurred in the preparation of your proposals, or to procure or contract for any articles of goods or services.

2.	Scope of Service

  - Fees. Contractor is responsible for all permits, fees, inspections, certifications and approvals necessary to demolish the buildings as outlined by the standards established by federal, state, and local authorities. This is school district property. Any Profit and Overhead of change orders will be held to 10% above actual cost.

  - Utilities and Terminations.  Prior to commencement of work by Contractor, OSD will conduct all utility terminations, power/phone/cable disconnections,  as well as be responsible for any service or termination fees (if applicable) on each parcel of property within the Demolition Area, not including mainlines. Lateral water lines will be terminated at meter vault.  Contractor will cap sewer laterals at property line on each parcel of property at the time of building demolition. All lateral lines (sewer, water, etc.) from disconnection point to the building shall be removed and disposed of on each parcel of property by Contractor. Oak Street water and sewer are private lines. Addresses on Oak Street will be terminated at Oak Street. Contractor shall arrange for termination of Oak Street water and sewer at Madison Ave. Soils inspections and testing will be required and will be paid for by OSD.

  - Asbestos Abatement and Inspection Report.  The structures will be vacated, asbestos abatement conducted, and asbestos reports will be provided to the demolition contractor. OSD will prepare an asbestos inspection report for each property, and will coordinate abatement prior to issuing notice to proceed to Contractor. No asbestos bids are required of contractor with the initial bid. The asbestos inspection report and verification of any abatement activity will be provided to Contractor along with notice to proceed. Contractor must have a current license/certification for asbestos and hazardous material removal for a demolition contractor.

  - State Permits and Notices.  Obtain “10-Day Notification” permit from the Utah DAQ prior to any demolition work.

  - Storm Water Pollution Prevention Plan. A State issued SWPPP permit must be obtained by the Contractor for this project. The submission, permitting, and ongoing implementation and maintenance of SWPPP shall be the responsibility of the Contractor. A SWPPP will be required for the entire Demolition Area and must be submitted, approved, and permitted prior to commencement of demolition.

  - Demolition and site clearance. Contractor shall demolish and remove all above and below ground debris and appurtenances including but not limited to; the main structure and/or any detached structures, all basements, footings, foundations, floors, porches, private sidewalks and debris of any kind.  Contractor shall include the demolition and removal of all parking slabs, concrete and/or asphalt flatwork (not including city sidewalk and curb/gutter), accessory/ detached structures, sheds or garages, trees (except trees in park strips), or any underground piping,  junk, trash or dead trees which may be present.  No debris shall be left or buried on the site.  Demolition methods must include a means of controlling dust generated on the site. Should these means include the use of water, the rental of an Ogden City water meter and cost of water will be the responsibility of the Contractor. AT NO TIME SHALL CONTRACTOR HOOK INTO A MUNICIPAL WATER SOURCE (HYDRANT) WITHOUT CITY APPROVAL AND THE REQUIRED METER. All removal from this site of debris, rubbish, and other materials resulting from demolition operations must be disposed of in a legal manner.

  - Green Waste: Contractor will remove all trees and plant material, except park strip trees.  Tree removal shall include completely removing tree stumps.

  - Backfill and Compaction. Excavated areas associated with the removal of all substructures should be backfilled with a well-graded granular material having a maximum size of 2 inches and not more than 15 percent passing a #200 sieve. All earth materials placed in excavated areas should be placed in maximum eight inch loose lifts and densified to an in-place unit weight equal to 95% of the Maximum Laboratory Density as determined by ASTM D 1557-78. Inspections required after demolition and prior to backfill as per the soils report.

  - Environmental Contaminant Discovery.  Underground hydraulic, oil or gas tanks may be present in the Demolition Area. Upon discovery of any UST, Contractor will

- Stop all Work associated with discovery

- Notify OSD

- Identify size and location of tank

- Determine levels of contaminants

- Wait for OSD approval and further instructions

  - Project Schedule.  The project will proceed in two phases. The structures will be vacated, asbestos abatement conducted, and utility lines killed over a three to four-month period of time by OSD.

The first phase involves removal of the structures and utility lines with sewer line cap, and backfill/compaction. Each individual lot will be awarded on a Notice to Proceed. Contractor shall complete demolition of structure(s) on each individual parcel within seventeen (17) calendar days of Notice to Proceed.

The second phase involves removal of all remaining appurtenant material. This phase will be awarded with a Notice to proceed after all structures are demolished. This phase shall be completed and all debris and equipment removed from site within 14 calendar days from notice to proceed (subject to change).

  - Dumping Requirements: All demolition debris must be taken to a licensed landfill. All landfill receipts (for general debris and hazardous waste) must be turned in before final approval and payment.

  - Infrastructure Protection: Protect City sidewalk, drive approaches, curb/gutter and street by means acceptable to Ogden City Engineering. Contractor will be liable for any damage to public property.

  - Salvage and Recycling: Salvage rights belong to the Contractor after Notice to Proceed is issued. All portions of the demolitions must be removed, to include scrap metals, concrete, and other materials. Contractor may sell any and all materials and retain any proceeds from the sale of such materials. It is the expectation of OSD that any proceeds earned by Contractor through recycling or salvaging will offset the costs of their services.

  - Safety: .Public safety must be considered at all times. The Contractor must take precautions at all times to utilize and store materials and equipment in a way that will prevent injury to citizens. Before leaving for the day, Contractor must ensure that proper signs, caution tape, physical barriers or other devices as needed to signal a hazard or restrict public access are in place. In addition, the Contractor must insure the safety of their workers by adhering to industry best practices, OHSHA safety, and traffic safety guidelines as applicable for the activity being performed. The OSD-designated Project Manager reserves the right to temporarily stop work if they see an unsafe practice and to suspend work until the issue is addressed.

  - Record on Record Document location and extent of all capped and abandoned lines below grade.

- Outline of Expectations

  - Significant experience in demolition and removal of residential and commercial site debris, backfill and grading. The successful bidder shall clearly possess an understanding of the scope of work required including:

- Permitting and clearances

- Asbestos/Universal Waste abatement. Eight-Hour OSHA Class II Asbestos Removal certification.

- Demolition site clearance and backfill/ site grading.

- Project completion documentation.

- Possess the required licenses, insurance, bonding, etc.

3.2	Contractor will assure that all permitting, abatement, demolition and debris removal will comply with applicable City, State and Federal regulations and procedures covering demolition, i.e., Utah Dept of Environmental Quality, OSHA, Utah Labor Commission, Federal Department of Transportation and Utah Department of Air Quality.

- Special Instructions

  - Project Demolition Order & Activities.  Demolition shall commence with specific buildings within the Demolition Area as directed by OSD.  OSD reserves the right to designate none or any number of the separate parcels for demolition.  Contractor must be cognizant that some buildings commencement of demolition and shall accommodate those parties as reasonable as possible.

  - Fee Estimate. Proposals should include a detailed cost breakdown of all proposed fees and must break out the fees for each property – see Attachment 1 – Bid Worksheet.   OSD reserves the right to demolish none, all or any number of individual property parcels.

  - Operating Hours: Work shall be performed between 7am and 7pm only. No work shall be performed on Sundays unless authorized in advance by OSD.

- Contract Document OSD will negotiate a Professional Services Agreement with the winning Contractor.

- Insurance Requirements Contractor shall procure and maintain for the duration of the contract insurance against claims for injuries to persons or damages to property which may arise from or in connection with the performance of the work hereunder by Contractor, its agents, representatives, employees or subcontractors.  The cost of such insurance shall be included in Contractor’s bid.  The amount of insurance shall not be less than:

1.	Commercial General Liability:  $1,000,000 combined single limit per occurrence and $2,000,000 general aggregate for bodily injury, personal injury and property damage.

2.	Business Automobile Liability:  $1,000,000 combined single limit per accident for bodily injury and property damage for owned, non-owned and hired autos.

3.	Workers’ Compensation and Employers’ Liability:  Workers’ compensation limits as required by the labor code of the State of Utah and employers’ liability with limits of $1,000,000 per accident.

Each insurance policy required by this Agreement shall contain the following clauses:

-This insurance shall not be suspended, voided, canceled, reduced in coverage or in limits except after thirty days prior written notice by certified mail, return receipt requested, has been given to OSD.

-It is agreed that any insurance or self-insurance maintained by OSD, its elected and appointed officials, employees, agents and volunteers shall be excess of Contractor’s insurance and shall not contribute with insurance provided by this policy.

Each insurance policy required by this Agreement, accepting policies for Workers’ Compensation and Professional Liability shall contain the following clause:

-Ogden School District, its elected and appointed officials, employees, agents and volunteers are to be named as additional insurers as respect to operations and activities of, or on behalf of, the named insured as performed under Agreement with OSD.

Insurance is to be placed with insurers acceptable to and approved by OSD.  Contractor’s insurer must be authorized to do business in Utah at the time the contract is executed and throughout the time period the contract is maintained, unless otherwise agreed to in writing by OSD.  Failure to maintain or renew coverage or to provide evidence of renewal will be treated by OSD as a material breach of contract.

OSD shall be furnished with original certificates of insurance and endorsements effecting coverage required within, signed by a person authorized by that insurer to bind coverage on its behalf.  All certificates and endorsements are to be received by OSD before work commences.

OSD reserves the right to require complete, certified copies of all required insurance policies at any time.

Any deductibles or self-insured retentions must be declared to and approved by OSD.  At the option of OSD, either: the insurer shall reduce or eliminate such deductibles or self-insured retentions as respects OSD, its elected and appointed officials, employees, agents and volunteers; or Contractor shall provide a financial guarantee satisfactory to OSD guaranteeing payment of losses and related investigations, claim administration and defense expenses.

Contractor shall include all subcontractors and insured under its policies or shall furnish separate certificates and endorsements for each subcontractor.  All coverage for subcontractors shall be subject to all of the requirements stated herein.

Nothing contained herein shall be construed as limiting in any way the extent to which Contractor may be held responsible for payments of damages to persons or property resulting from Contractor’s or its subcontractor’s performance of the work covered under this Agreement.

Bid bonds will be required at time of bid.

- Furnishing of W-9: Payment under this Agreement is contingent upon Contractor furnishing OSD with a signed and completed W-9 IRS tax form. Contractor shall cooperate with OSD in furnishing any additional information OSD may need to comply with rules and regulations of the Internal Revenue Service.

- Evaluation and Award The contractor selection will be based on proposed Contractor pricing.  Price will be based on the total bid amount and not parcel by parcel.

OSD reserves the right to accept or reject any bid that best serves its convenience and/or is found to be in its best interest.  OSD encourages and welcomes bids from women-owned and minority-owned businesses. Bidders must be in good standing with OSD.

- Bid Submittals Those wishing to submit a bid for the project must provide, at a minimum, the following items:

- Completed bid worksheet (Attachment 1). Note the bid form is laid out in a specific manner. Please structure your bids accordingly.

- Documents showing appropriate certification in appropriate OSHA Class for asbestos removal.

- Proof of all other appropriate professional licensing as required by the State of Utah

- If applicable, documents showing pre-certification as a woman-owned, minority owned, small, or disadvantaged business

- A disposal and recycling plan for all structures and debris removed from the site

- Proof of Insurance: General Liability, Workers Comp, Automobile (must be current)

- BONDS:  A certified check or bid bond of not less than five percent [5%] of the amount of the bid is to accompany the bid. The bid bonds of the unsuccessful bidders will be returned within 5 days after the award of the bid.  The Board of Education will also require a 100% full performance and 100% full payment bonds.

IF YOU REQUIRE ADDITIONAL INFORMATION:

Questions related to the proposal or regarding the bid process should be directed to Ken Crawford at crawfordk@ogdensd.org or through bidsync. Please communicate via email so there is a record of correspondence.

Attachments:

- BID WORKSHEET

- DEMOLITION AREA

| Attachment #1 |  |  |  |
| --- | --- | --- | --- |
| Demolition Bid Worksheet |  |  |  |
| Tax ID# | Address | Land Sq. Ft | Building Bid | Land Bid |
| 01-037-0001 | 684 22nd Street | 6040 |  |  |
| 01-037-0003 | 670 22nd Street | 5445 |  |  |
| 01-037-0005 | 662 22nd Street | 8662.5 |  |  |
| 01-037-0006 | 658 22nd Street | 6187.5 |  |  |
| 01-037-0007 | Vacant Land | 1980 |  |  |
| 01-037-0008 | 650 22nd Street | 6105 |  |  |
| 01-037-0009 | 644 22nd Street | 7012.5 |  |  |
| 01-037-0039 | 641 21st Street | 6534 |  |  |
| 01-037-0040 | 653 21st Street | 6006 |  |  |
| 01-037-0043 | 667 21st Street | 4356 |  |  |
| 01-037-0044 | 667 21st vacant land | 480 |  |  |
| 01-037-0045 | 2105 Madison | 4800 |  |  |
| 01-037-0046 | 2107 Madison | 7920 |  |  |
| 01-037-0047 | 2121 Madison | 8580 |  |  |
| 01-037-0048 | 2125 Madison | 5412 |  |  |
| 01-037-0049 | 2129 Madison | 15006.75 |  |  |
| 01-037-0050 | Vacant Land & Garage | 13282.5 |  |  |
| 01-037-0051 | 2137 Madison | 5445 |  |  |
| 01-037-0052 | 2145 Madison | 8167.5 |  |  |
| 01-037-0053 | 2149 Madison | 10890 |  |  |
| 01-037-0054 | 660 Oak | 8277.5 |  |  |
| 01-037-0055 | 658 Oak | 4810 |  |  |
| 01-037-0056 | 652 Oak | 4810 |  |  |
| 01-037-0057 | 648 Oak | 4752 |  |  |
| 01-037-0058 | 655 Oak | 5350.125 |  |  |
| 01-037-0059 | 657 Oak | 3795 |  |  |
| 01-037-0061 | 668 22nd Street | 6600 |  |  |
| 01-037-0002 | 2165 Madison | 6417.5 |  |  |
| 01-037-0004 | Vacant Land | 2722.5 |  |  |
| 01-037-0060 | Vacant Land & Shed | 10890 |  |  |
| 01-037-0063 | Vacant Land | 4537.5 |  |  |
| 01-037-0067 | 659 21st Street | 9240 |  |  |
| ROW | 600 Oak Street | 7314 |  |  |
|  |  | Total |  |  |
|  | Buildings & Land |  |  |  |
|  | SWPPP |  |  |  |
|  | Permits & Fees |  |  |  |
|  | OH & Profit |  |  |  |
|  | Total Bid |  |  |  |
|  | Included in this bid is 100 yards of additional demolition of debris at: |  | Per yard. |  |

Included in this bid is 100 yards structural fill at: per yard.

Any of the 100 yards of additional demolition of debris or structural fill that is not used will be credited back to the district!

I hereby warrant and represent that the information presented in this proposal is true, accurate and complete.

Company:  ___________________________________

By:             ___________________________________

Title:           __________________________________

Date:          ___________________________________

ATTACHMENT 2 – ‘DEMOLITION AREA’