Ogden City School District

Request for Proposal

Taylor Canyon Elementary School

Electrical / Telecommunications

RFP # 10-014

Surface Raceway, Cable Management,

End to End Category 6, 450 MHz System

1950 Monroe Blvd.

Ogden, Utah

March 12, 2010

Invitation for Proposals

Notice is hereby given that Ogden City School District is inviting proposals to provide services for Taylor Canyon Elementary School at 2130 Taylor Ave, Ogden, Utah 84401.

Telecommunications

- Category 6, 450 MHz Plenum cable, all horizontal lines

- Category 6, 450 MHz Patch Cables

- Hubbell Cat 6 patch panels

- 4 Post Rack with vertical wire management (19”x32”) MDF

- Ladder rack support to wall is required for 2 and 4 post racks

- Hubbell category 6 modular jacks (Voice – Gray, Data - Black) (keystone)

- Hubbell face plates to match raceway or equivalent

- 12 Stand, 62.5 micron multimode fiber cable, SC termination required

- 19” rack mounted LIU required

- Hubbell wall mounted RE unit required for Portable

Electrical

- Hubbell PS3 Series Raceway (3-channel) where required

- Hubbell PS3 series accessories where required (boxes, plates, etc.)

- Wiremold / Evolution Poke-Thru 6”x6”

- 20 AMP circuit per 4 computers.

- Power sub panel if required.  Must support future expansion.

Bids will be received by the Board of Education of Ogden City School District.  Bids will be in accordance with specifications prepared by Technology Supervisor. Bids will be accepted for all areas of RFP only. Bid must list all line items with quantity and amounts separately.

The Board of Education of Ogden City School District reserves the right to reject any or all bids or to waive any information or technicality in any bid in the interest of the District.  Contractor liable for damage caused during installation.  The Board of Education of Ogden City School District reserves the right to terminate this project without cause.

A Pre-Bid walk through meeting will start at Taylor Elementary main office at 2130 Taylor Ave, Ogden, Utah 84401, on March 25, 2010.  The meeting will start at 9:00 AM.  We will visit all rooms after initial meeting and attendance at walk through is mandatory to qualify to bid project.  Documents provided by Ogden District.

Sealed bids must be delivered no later than 2:00 pm Mountain Time April 9, 2010 and have written on the outside of the envelope RFP 10-014.  Proposals will be accepted in the office of the Purchasing Director at the Ogden City School District Administration Building, Room 209, 1950 Monroe Blvd. Ogden, Utah 84401-0619.

Anticipated start of project will be May 3, 2010 and must be completed by June 18, 2010.

  - Telecommunications Proposal

- Scope of work

1.	The contractor (Telecommunications / Electrical) shall supply all labor and material for a complete functional system as described herein. It will include installing all cabling, conduit or surface molding, faceplates, boxes, 20A 120V circuits, sub panels, grounding cables, vertical wire management, rack mounted patch panels, modular jacks, racks, 2 meter category 6 450 MHz patch cables, 62.5 micron 12 strand fiber with LIU and SC termination.

2.	The contractor shall test, document and warranty system.

- Equipment

  - 4 post rack with vertical wire management (MDF)

  - Ladder rack support to wall is required, 2 and 4 post racks

  - Hubbell category 6 patch panels

  - Hubbell category 6 modular jacks (Voice – Gray, Data - Black) (keystone) and Gray is always top left corner.

  - Labeling is required at technology closets (MDF) and all termination points. Patch panels and jacks.

  - Horizontal wire management

  - 2 – 2 meter patch cables, category 6, 450 MHz, per horizontal cable

- System Requirements

  - All horizontal cabling will be category 6, 450 MHz plenum cable

  - Maximum horizontal run will be 295 feet

  - Follow the EIA/TIA 568B standard

  - Conduit and or surface molding (no exposed cabling in classrooms except patch cable to device). Hubbell surface molding preferred.

  - Grounding cable to all racks

  - All equipment locations specified by Ogden School District Technology Supervisor or Network Engineer only.  No changes without their authorization.

  - Cable support must be provided to specifications in tunnels

  - Voice over Ethernet Jack must be Gray

  - Data Jack must be Black

  - Top left jack must be Gray

  - All Voice over Ethernet jacks must terminate on their own patch panel

  - Horizontal Cabling: Voice cables must have different color than data.

  - VGA HD-15 / Audio cabling must be terminated in wall mount boxes with plates.

  - VGA HD-15 runner cables must be Cables to Go RapidRun plenum

  - Audio from ceiling mounted sound system to Document Camera location and to projector

  - Provide power to center of ceiling for Sound System

  - Provide power to wall for Interwrite Board location

- Room 4 Lab

  - Provide 36 data drops for lab to MDF

  - Wiremold / Evolution Poke-Thru (6)

  - Provide 4 data drops at teacher location

  - Provide 4 data drops at alternate location

  - Provide power to poke-thru for 36 computers at 4 per 20 AMP circuit

  - Provide two meter category 6 patch cables per data drop

- Room 17 TEC Lab

  - Provide 16 data drops for lab to MDF

  - Wiremold / Evolution Poke-Thru (4)

  - Provide 4 data drops at teacher location

  - Provide 4 data drops to alternate location

  - Provide power to poke-thru for 16 computers at 4 per 20 AMP circuit

  - Provide two meter category 6 patch cables per data drop

- Room 18 TEC Lab

  - Provide 16 data drops for lab to MDF

  - Wiremold / Evolution Poke-Thru (4)

  - Provide 4 data drops at teacher location

  - Provide 4 data drops to alternate location

  - Provide power to poke-thru for 16 computers at 4 per 20 AMP circuit

  - Provide two meter category 6 patch cables per data drop

- Provide to all standard classrooms

  - Provide 4 data drops front of classroom to MDF

  - Provide 4 data drops back of classroom

  - Provide two meter category 6 patch cables per data drop

- Provide to all main office locations

  - Provide 4 data drops per location

  - Provide two meter category 6 patch cables per data drop

- Provide Video/Audio to designated classrooms (1-9, and 12-22).

  - Provide VGA HD-15 and Audio from projector to Teacher location

  - Provide VGA HD-15 from projector to Document Camera and Audio

  - Provide Audio from ceiling mounted sound system to Projector

  - Provide power to wall mounted projector above Interwrite Board

  - Provide power to ceiling mounted sound system

- Provide new IDF in Portable

  - Provide Hubbell wall mounted RE Unit

  - Provide new category 6 patch panel(s)

  - Provide 4 data drops to front of classroom

  - Provide 4 data drops to back of classroom

  - Provide 12 strand 62.5 micron fiber to MDF.

  - Provide new SC terminated rack mounted LIU, IDF & MDF.

- Provide new 4 post rack for MDF

  - Provide 4 Post Rack with vertical wire management, installed

  - Provide ladder rack or other appropriate wire management for MDF

  - Provide new category 6 patch panel(s)

  - Provide one horizontal wire management per patch panel

  - Mount all new fiber LIU to this 4 port rack

  - Provide ground to rack

  - Provide 6, two meter SC to LC fiber patch cables

  - Provide 6, two meter SC to SC fiber patch cables

- Contact Information

  - Contact Ogden School District Technology Supervisor at dont@ogdensd.org or cell phone 801-430-1283

  - Alternate Contact:  Mike Hipwell HipwellM@ogdensd.org